## Slide 1: Computer Aided Design CAD
Lecture 3

## Slide 2: Network Equilibrium Equations
Loop equations: A branch of a network can, in general, be represented as shown in Figure
where EB is the voltage source of the branch.
IB is the current source of the branch
ZB is the impedance of the branch
JB is the current in the branch

## Slide 3: Network Equilibrium Equations
The voltage-current relation is then given by
VB =(JB + IB ) ZB − EB
For a general network with many branches, the matrix equation is
VB = ZB (JB +IB ) − EB => VB = ZB (IB + Is) – VS (1)
Where VB , JB , IB , and EB are B × 1 vectors and ZB is the branch impedance matrix of B × B

## Slide 4: Network Equilibrium Equations
Each row of the tie-set matrix corresponds to a loop and involves all the branches of the loop. As per KV L, the sum of the corresponding branch voltages may be equated to zero. That is
BVB =0 (2)
where B is the tie-set matrix.
In the same matrix, each column represents a branch current in terms of loop currents. Trans- posed M is used to give the relation between branch currents and loop currents.
JB = BTIL (3)
This equation is called loop transformation equation.

## Slide 5: Network Equilibrium Equations
Substituting equation (1) in (2),
VB = ZB (JB +IB ) − EB (1)
BVB =0 (2)
we get
BZB {JB + IB }−BEB = 0 (4)
JB = BTIL (3)
Substituting equation (3) in (4)
we get
BZB BTIL + BZB IB − BEB = 0
BZB BTIL = BEB − BZB IB => BZB BTIL = BVS − BZB IS

## Slide 6: Network Equilibrium Equations
Get VB branch voltage and JB branch current using cut-set matrix
Each row of the cut-set matrix corresponds to a particular node pair
voltage and indicates different branches connected to a particular node. KCL can be applied to the node and the algebraic sum of the branch currents at that node is zero.
CJB =0 (5)
Each column of cut-set matrix relates a branch voltage to node pair voltages. Hence,
VB = CTEN (6)

## Slide 7: Network Equilibrium Equations
Current voltage relation for a branch is.
JB = YB (VB +EB ) −IB
For a network with many branches the above equation may be written in matrix form as,
JB = YB VB + YB EB − IB (7)
where YB is branch admittance matrix of B × B.

## Slide 8: Network Equilibrium Equations
Substituting equation (7) in (5)
CJB =0 (5)
JB = YB VB + YB EB − IB (7)
We get
CYB VB + CYB EB − CIB =0 (8)
Substituting equation (6) in (8)
VB = CTEN => VB = CT VT (6)
We get
CYB CTEN = C (IB − YB EB ) => CYB CT VT = C IS − C YB VS )

## Slide 9: Example
For the network shown in Figure write a tie-set matrix and then ﬁnd all the branch currents and voltages.